## Slide 1: Measuring the Efficiencies of Tow Plows and Wing Plows
Duane Bennett and Dr. Ty Lasky
Advanced Highway Maintenance & Construction Technology (AHMCT) Research Center, UC Davis
January 19, 2022
Clear Roads CR19-03, Contract # 1034818
Tasks 10: Decision Support Tool User’s Guide

## Slide 2: User's Guide Viewing
DST User’s Guide viewing
The Decision Support Tool (DST) User’s Guide PowerPoint program consists of a series of PowerPoint slides grouped by subject and separated by section breaks. The next slide has category buttons that enable a user to go to the subjects of interest and return to the category slide. The user can also elect to step through the entire user’s guide by skipping past the return slides.

## Slide 3: Decision Support Tool (DST) User’s Guide Categories
DST Program Information
Click Topic for Detailed Explanation
General Description
Installation Guide
Program Overview
Plow Cost/Performance Data
Plow Route Data
Running Analyses
DOT Applications
Video 1: User Guide Navigation

## Slide 4
End of User’s Guide Overview
Next presentation slide is the beginning of the DST General Description section

## Slide 5: DST General Description
Project description
Measuring the Efficiencies of Tow Plows and Wing Plows was a Clear Roads (CR) consortium Department of Transportation (DOT) pooled fund research project. This research was performed by the Advanced Highway Maintenance and Construction Technology (AHMCT) Research Center at the University of California-Davis.
DST overview
The Decision Support Tool (DST) is an Excel program that quantitatively calculates highway snow plowing efficiencies and life cycle plow configuration costs based on real-world plowing data. It provides DOT users with an innovative method of analyzing both their current plow deployment strategies and project the potential cost benefits of new plow type procurements. The DST primarily consists of several cost and performance data libraries, a plow route configurator, and a user interface. The DST calculates plow efficiency based on the customizable cost and performance data libraries and user-defined plow allotment and plow route. The DST analysis assists DOTs with calculating a return on investment of the designated plow types based on their state-specific costs and plow configurations.
User Interface Screen

## Slide 6: DST General Description
How the DST works
The DST enables a user to quantitatively calculate the average costs of clearing a user-defined plow route from a user-supplied allotment of plows.
Roadway Segments: Sections of roadway between geometric nodes consisting of lanes and shoulders. Segment data library can be customized by the user.
Plow Allotment: User selects plows to be utilized in the DST calculation
Plow Route: User creates plow route by selecting roadway segments and geometric nodes from data libraries
Geometric Nodes: Diverges or redirections in the roadway. The geometric node data library can be customized by the user.
DST Results
Geometric Nodes
Roadway
Segments
User Interface

## Slide 7: DST General Description
DST results – Measure of Plow Efficiency
The DST calculates the most cost efficient grouping of user-allotted plows to clear a user-defined plow route.
See Full List: For each plow instance the DST calculates a full list of daily operating costs in ascending order for all plow deployment permutations. Usually only the first few lines are the focus of interest.
Through Lanes Cleared Right Data Screen
When analyzing a plow route containing multiple plow instances, the user may need to examine the detailed cost data and consult a DOT’s specific plowing procedures when determining the most efficient group of plows to deploy.
The DST calculates the daily operating cost for every permutation of the allotted plow combinations necessary to clear the entire width of the user-defined plow route at its widest point. The DST makes separate calculations for each of the four plowing functional instances as to how each plow will utilized:
1) Through lanes cleared right
2) Through lanes cleared left
3) Diverge lanes cleared right
4) Diverge lanes cleared left
Widest Point
Through Lanes
Diverge Lanes

## Slide 8: DST General Description
DST results – Life Cycle Costs
The DST calculates plow life cycle cost for each of the six designated plow types over a user-defined duration provided for direct comparison purposes.
User Interface Screen

## Slide 9: DST General Description
What the DST does
Ranks cost efficiency of plow types and groups of plow types necessary to clear the full width of a specific plow route.
Analysis data is normalized to support direct comparisons between plow type efficiencies.
User can create custom-defined plow route containing user-defined roadway segments and roadway geometrics.
User can configure custom plow configurations based on designated plow types.
User can customize the plow cost, performance, and service data for the configured plows.
User allocates the types and quantities of user-defined plow configuration(s) to be utilized in the plow efficiency analysis comparison.
DS Tool calculates the average time required to plow the user-defined plow route based on the speed of the slowest plow and the total route length.

## Slide 10: DST General Description
What the DST does not do
Does not explicitly solve for the best combined plow deployment grouping for the entire roadway.
Does not arrange plows within a “most efficient” plow grouping.
Does not calculate specific DOT plowing operating costs for specific DOT deployments.
Does not account for uncommon or extraordinary DOT plowing applications.
Does not configure all plows in a DOT’s fleet.

## Slide 11: DST General Description
Contact Information
Project champion:
Doug McBroom
Montana DOT
dmcbroom@mt.gov 406-444-6157
Clear Roads Project Manager:
Greg Waidley
CTC & Associates
greg.waidley@ctcandassociates.com 608-490-0552
Project Principal Investigator
Ty Lasky
AHMCT Research Center
talasky@ucdavis.edu 530-752-6366

## Slide 12
End of DST General Description Presentation
Next presentation slide is the beginning of the DST Installation Guide section
Click here to return to Main Category Page

## Slide 13: DST Installation Guide
The DST is available for download at…
https://clearroads.org/download/decision-support-tool-2/
The Clear Roads 19-03 Plowing Efficiency Decision Support Tool (DST)
The DST is an Excel spreadsheet file which must be run on a computer with the Microsoft Excel 2016 application installed.

## Slide 14: DST Installation Guide
DST program launch
Once the DST program is launched, the user may be confronted with a series of Excel security notices which the user must click on to accept to run the program. Which warnings are displayed depends on several factors, including Excel version and individual or organizational security settings.
Accepting the Enable Editing security warning enables the user to customize DST data.

## Slide 15: DST Installation Guide
Enable Macros
The DST program utilizes Visual Basic code to calculate plow grouping permutations. The user needs to click on the Enable Content security warning to enable the DST program to run.

## Slide 16
End of DST Installation Guide Presentation
Next presentation slide is the beginning of the DST Program Overview section
Click here to return to Main Category Page

## Slide 17: DST Program Overview
DST program description
The DST plow efficiency calculation includes the metrics of time, level of service, labor allocation/optimization, and width of roadway cleared in a single pass. The efficiency calculation also incorporates individualized calculations for each piece of equipment including maintenance, consumables, equipment life, usage, and seasonal and operational cost data. The DST program solves for the necessary plow type(s), or combination of plow types to clear the entire width of the route at its widest and calculates the corresponding operational cost. The efficiency algorithm utilizes DOT-customizable data libraries that define the plow equipment performance and cost parameters for the six plow types as well as specific plow route roadway geometries.
User Interface Screen

## Slide 18: DST Program Overview
DST program flow
The DST Excel program consists of several sheets which are integrated together to perform the plow efficiency analysis. The plow efficiency calculation utilizes user-customizable cost and performance data contained in several data libraries. The three main data libraries are the Plow configuration data, plow operating costs data, and the defined plow route. The defined plow route library is further comprised of route segment data and route geometry data. All the data in each of the libraries is user customizable.

## Slide 19: DST Program Overview
Customizing the data libraries
On the DST User Interface screen, there are navigation arrows that take the user to the various separate cost and performance data libraries along with an arrow that takes the user to the define plow route section of the program.
Note: The navigation arrows may sometimes need to be clicked on twice depending on the last program function executed. This is an Excel behavior.
User Interface Screen

## Slide 20: DST Program Overview
Running DST analyses
The DST analysis is run from the User Interface page. On this page the user can only change the plow quantities of configured plows to be used in the analysis. The configured plow types listed on the Plow allocation table and route statistics are set on their associated data pages. The analysis examines all permutations of the allocated plows that clear the entire roadway in a single pass and determines their daily operational cost.
If a single plow is to make multiple runs to clear the roadway, the user should allocate multiple plows of the same type. The analysis will then determine the minimum number of plows required to clear the roadway and at what cost. This can also represent the number of trips and overall cost for a single plow deployment, but the user would have to multiply plow route time by the number of trips.
User Interface Screen

## Slide 21: DST Program Overview
DST analysis results
The plow efficiency analysis methodology divides a plow route into four distinct instances and calculates the most efficient daily cost plow configuration for each. If the user-defined plow route does not contain one or more of the four instances, then the results for those instances are left blank.
Combining plow instance results
The plow efficiency analysis results from each of the four plow instances cannot be simply combined to establish the most efficient plow echelon. The user should consult the full result lists taking into consideration a DOT’s particular operational and safety practices in determining the most appropriate plow combination.
User Interface Screen

## Slide 22: DST Program Overview
Establishing efficient plow echelons
The DST User Interface page has a “See Full List” button for each plow route instance. When selected the user can view the full list of plow combinations permutations ranked in ascending order of daily operating cost for the defined plow route. By consulting the first few lines of the list(s) for each plow route instance, and considering a DOT’s specific plowing procedures, a user can logically ascertain what is the best plow echelon for a DOT to deploy on a specific plow route.
User Interface Screen
Through Lanes Cleared Right Data Screen

## Slide 23: DST Program Overview
DST Life Cycle Analysis
The DST analysis includes a calculation of the average plow life cycle costs by plow type for comparison purposes.
The plow life cycle algorithm averages the cost data of all the plows configured in each plow type category in the data library. Equipment costs, service life and salvage values are the key data utilized in the life cycle calculation. The averaged plow type costs are then normalized in respect to the user-defined duration, so direct comparisons between plow types with different service lives can be readily examined. The analysis is calculated on the basis of a user-defined deployment duration which serves as the common reference frame which normalizes the costs of plows with different expected equipment service life spans. The life cycle calculation is based solely on plow costs and is plow route-independent.
User Interface Screen

## Slide 24
End of DST Program Overview Section
Next presentation slide is the beginning of the DST Plow Configuration Data section
Click here to return to Main Category Page

## Slide 25: DST Plow Cost and Performance Data
Define plows for the DST analysis
The plow truck/tow plow configuration, cost, and performance presented in the plow allocation table on the DST user interface screen is defined in the plow configuration and plow operating cost data libraries. The yellow navigation arrows take the user to the plow data libraries.
To Plow Configuration Data Library
To Plow Operating Cost Data Library
Data from Plow Configuration and Performance Data Libraries
User Interface Screen

## Slide 26: DST Plow Cost and Performance Data
Customizing DST plow configuration data
The plow truck/tow plow configuration data library is divided into sections that represent each of the six project designated plow types. The data library has default configurations that enables a user to change, add, or remove plow configurations, costs and descriptions as necessary to be consistent with a DOT’s specific plowing operations. The named plow types then appear in the plow allocation table of the user interface screen where they can now be selected for inclusion in analysis runs. The plow configuration data library also includes salvage value and expected service life data which is utilized in the life cycle calculation. All the customized plow configuration data is saved for future use. When modifying plow configuration data, it is essential to do so in the section matching that plow type.
Video 2: Customizing Plow Configuration Data

## Slide 27: DST Plow Cost and Performance Data
Customizing plow operational cost data
The plow truck/tow plow operational cost data library contains the associated operational costs to operate the plow configurations defined in the plow configuration library. Cost data is divided into seasonal and daily costs. The data library has default costs that a user can customize to reflect a DOT’s specific plowing operational costs. The amalgamated plow costs appear in the plow allocation table as a daily operating cost estimate for the efficiency calculation. In the operational data library are also values for plow speed and plow usage estimates. This data is utilized for estimating plow route loop times and to convert seasonal equipment costs to a daily basis. The customized plow configuration data is saved for future use.
Video 3: Customizing Plow Cost/Performance Data

## Slide 28
End of DST Plow Configuration Data Section
Next presentation slide is the beginning of the DST Define Plow Route section
Click here to return to Main Category Page

## Slide 29: DST Plow Route Data
Defining plow route
The DST calculates plow efficiencies on a plow route basis. The user must define a plow route to run a DST analysis.
Plow routes are defined in the DST as a combination of roadway segments and geometric nodes. The user can assess the roadway segment and geometric node library data using the navigation arrows on the plow route table. These libraries contain default data that the DOT user can customize to define important highway features that impact plowing operations. The customized data is saved and appears on the plow route definition table. The user defines the plow route to be used in the analysis by selecting the route segments and geometric nodes that describes a real or representative highway plow route.
User Entry
Customized DOT Geometric Data
Define Plow Route Screen
Segment Data Screen
Geometric Node Data Screen

## Slide 30: DST Plow Route Data
Customizing segment data
Highway plow routes consist mainly of long stretches of multi-lane pavements with shoulders. Roadway segments are defined as a combination of the number and width of traffic lanes and the width of shoulder clearing on both sides of the direction of travel. The segment library contains only two factors from the segment data contribute to the plow efficiency calculation.
Overall segment clearing width
Segment length
Other segment information may be valuable for a DOT when selecting the allocated plow types, or deployment strategies, but these factors do not directly effect the efficiency calculation.
The DST has several common influential roadways geometries defined and default values are entered in the geometric data library. The user can customize these data values to better reflect a specific DOT’s highway plowing routes.
Video 4: Customizing Route Segment Data

## Slide 31: DST Plow Route Data
Customizing route geometry data
An important task to consider when defining a plow route for analysis is to identify and assign important roadway geometries. The user need not define every roadway geometric feature along the route, just the elements that contribute to:
Roadway clearing width
Diversion lanes
Plow times
Roadway geometries other than these may effect how a DOT plows the roadway, or allocates plows for analysis, but only the noted factors have a direct influence on the cost analysis and need to be defined for an accurate efficiency calculation.
The DST has several common influential roadways geometries defined and default values are entered in the geometric data library. The user can customize these data values to better reflect a specific DOT’s highway plowing routes.
Video 5: Customizing Route Geometry Data

## Slide 32
End of DST Define Plow Route Data Section
Next presentation slide is the beginning of the DST Run Analysis section
Click here to return to Main Category Page

## Slide 33: Running DST Analyses
Running DST analyses in three steps
The user defines a plow route for the DST analysis on the plow route definition screen.
The user switches to the user interface screen and selects a plow allotment for the analysis.
The user presses the Run button, and the DST calculates the most efficient deployment configuration.
The result of the DST analysis is then presented on the user interface screen in the most efficient plow deployment configuration table.
1
2
3
Result
User Interface Screen
User Interface Screen
Define Plow Route Screen

## Slide 34: Running DST Analyses
Step-by-Step DST efficiency analysis
To conduct a DST analysis, the DOT user would customize the plow configuration and operating cost data libraries if necessary.
The user customizes the plow configuration library data library.
The user customizes the plow operating cost data library.
Then the DOT user defines a plow route for the analysis.
3) Customize roadway segment data
4) Customize geometric node data
5) Define plow route
Once all the analysis data is customized, the user can run a variety of different plow efficiency and cost and comparison evaluations and iterate as needed.
6) Allocate plows to be included in the analysis
7) Run analysis
8) Examine results and full permutations list(s)
Video 6: Step-By-Step DST analysis

## Slide 35: Running DST Analyses
DST Life Cycle Analysis
The plow like cycle comparison calculation provides a normalized average life cycle cost that enables plows with different service life to be directly compared in reference to a DOT user selected duration.
The user only enters a common time period for the life cycle analysis and the program calculates the normalized value. The deployment duration is measured in terms of usage.
User Interface Screen

## Slide 36
End of DST Run Analysis Section
Next presentation slide is the beginning of the DOT Applications section
Click here to return to Main Category Page

## Slide 37: DOT Applications
DOT applications of the DST
The DST data and algorithms can be utilized in many ways to quantify various different aspects of DOT highway plowing cost efficiencies. The most prominent are:
Type-I Assist DOTs in determining the most cost-efficient plow deployment configurations for a specific plow route.
Type-II Provide a quantitative means for DOTs to determine the most efficient plow routes to deploy a specific plow type, or group of plow types.
Type-III Enable DOTs to compare the normalized plow life cycle cost between different plow types.
Type-IV Help DOTs to estimate their operating costs for specific plow type(s) for a given plow route

## Slide 38: DOT Applications
Type-I DST analysis
The Type-I DST analysis enables DOTs to determine the most efficient plow configurations for a specific plow route instance* and to make quantitative cost efficiency comparisons between the deployment of different plow types.
Video 7: Type-I DST analysis
* Plowing Instance: The four possible plow applications, clearing direction (Left – Right) and if plow route requires clearing of diverging lanes
The key element in a Type-I analysis is allotting an excess number of the plow types of interest for the plow route analysis to ensure sufficient clearing width capabilities of the most efficient plows. Allotted plows can be actually in a DOT’s fleet, or hypothetical. The DST then calculates the most cost-efficient group of plows by plowing instance. Then the user can navigate to the full details screen for each instance to examine the costs of all possible permutations of the allotted plows and make cost comparisons.

## Slide 39: DOT Applications
Type-I DST analysis – Single instance
Conducting a Type-I DST analysis on a single instance plow route, after running the analysis, the user navigates to the full results screen from the most efficient plow configuration to make cost comparisons between plow types.
Through Lanes Cleared Right Full Data Screen – Showing Only first 20 permutations
Ascending
Cost
Order
Plow type Cost comparisons
User Interface Screen - Single Instance Plow Route
The Type-I analysis comparison provides DOTs with a quantifiable cost saving effect of deploying specific plows to the analysis plow route and potentially justify the procurement of additional and different plow types.
The results of a single instance DST analysis can also be considered by DOTs as a guide for deployment of the most cost-efficient plow configuration on the specific plow route.

## Slide 40: DOT Applications
Type-I DST analysis – Multiple instances
Running the DST analysis on plow routes requiring multiple plowing instances solves for separate most efficient plow grouping for each instance.
User Interface Screen - Analysis Results for Multiple Instance Plow Route
Deployment Comparison Table Screen
A multiple instance DST analysis does not implicitly determine the overall most efficient plow grouping to deploy. The Type-I results need to be examined further from the perspective of a DOT’s plowing best practices to guide a DOT in determining the most appropriate plow grouping to deploy.
The “To Plow Combinations” button on the user interface screen navigates to the plow combination screen where the first ten permutations of each of the separate plow instance calculations are displayed along with the route statistics to simplify DOT plow deployment selection.

## Slide 41: DOT Applications
Type-I DST analysis – Multiple instances
The DST plow efficiency analysis is purely a mathematical evaluation. When a DOT is creating an actual plow grouping to deploy, the DOT user should consult the deployment plow comparison table. This table gathers together each of the separate instance results onto a single screen to aid in the selection of the plow combinations that might not necessarily be the most efficient but conform best with a DOT’s unique best plowing practices.
Minimum
Clearing
Widths
Select from the first few plow groups for each plow instance and combine into a single plow group to deploy
Deployment Comparison Table Screen

## Slide 42: DOT Applications
Type-II DST analysis
The Type-II DST analysis provides a quantitative means for DOTs to determine the most efficient plow routes to deploy a specific plow type, or group of plow types.
Video 8: Type-II DST analysis
The key element in a Type-II analysis is a particular plow configuration, or small group of plows of interest are allocated as the subject of the analysis, and the plow route becomes the variable. The DOT user can change the segments and geometric node data to make an evaluation between competing routes to determine which is route obtains the greatest efficiency from the plow configuration(s).

## Slide 43: DOT Applications
Type-II DST analysis – Tow Plow example
For this Type-II DST example the analysis determines a most efficient plow route for a Tow Plow.
User Interface Screen - First Plow Route DST Results
User Interface Screen - Second Plow Route DST Results
The same plows of interest are allotted for all analysis runs
Different plow routes produce a Tow Plow most efficient for the second route
Route #1
Route #2

## Slide 44: DOT Applications
Type-III DST analysis
The Type-III DST analysis enables DOTs to compare the normalized plow life cycle costs between different plow types.
For the Type-III analysis, a DOT user needs to enter a plow deployment duration for the analysis. The DST algorithm normalizes the different plow service life to obtain a comparable measure of cost on an even basis. The plow life cycle cost calculation is independent of plow route information.
Note: DOT plow usage is an important factor in the plow life cycle comparison calculation, but plow deployment routes are not taken into consideration.
User Interface Screen

## Slide 45: DOT Applications
Type-IV DST analysis
The Type-IV DST analysis helps DOTs in estimating their operating costs for specific plow type(s) for a given plow route.
For a Type-IV analysis, a DOT user simply enters a specific route and allots the plows, or group of plows they want to evaluate deployment to clear the route.
Note: The intended plow grouping may not always rank as the most efficient in the calculation and therefore not appear on the user interface screen. In this case the user will need to navigate to the see full list data screen to view the intended plow grouping daily operating cost value.
User Interface Screen

## Slide 46
End of DST User’s Guide Presentation
Click here to return to Main Category Page